## Slide 1
IPV6
By : Alan Saji

## Slide 2
Introduction to IP
  IP (Internet Protocol) is used to identify devices and enable communication on a network.
  Two versions of IP exist:
    IPv4 (Internet Protocol version 4) – older, limited addresses (32-bit).
    IPv6 (Internet Protocol version 6) – latest version, designed to replace IPv4.
  IPv6 provides more address space, better security, and modern features.

## Slide 3
What is IPv6?
  IPv6 = Internet Protocol version 6.
  It is a network layer protocol that allows devices to communicate over the internet.
  Uses 128-bit addressing, compared to IPv4’s 32-bit.
  Written in hexadecimal format, separated by colons (:).
  Example
2001:0db8:85a3:0000:0000:8a2e:0370:7334.
  Provides 3.4 × 10³⁸ unique addresses → practically unlimited.

## Slide 4
Abbreviation Rules in IPv6
IPv6 addresses are long, but rules make them shorter:
1. Remove leading zeros in each block.
  Example: 0074 → 74, 000F → F.
2. Replace consecutive zero blocks with ::.
  Example: 2001:0db8:0000:0000:0000:0000:0370:7334 → 2001:0db8::0370:7334.
Note: The shortcut :: can be used only once in an address.

## Slide 5
Addressing Methods in IPv6
IPv6 supports three addressing methods:
Unicast
One-to-One communication.
Multicast
One-to-Many communication.
Anycast
One-to-Nearest communication.
Each method is designed for different communication needs.

## Slide 6
Unicast Address
  A unicast address refers to a single host.
  When a computer wants to communicate with one destination, it uses a unicast address.
  Used for one-to-one communication.
  Examples:
    Sending an email to one person.
    Accessing a website hosted on a single server.

## Slide 7
Multicast & Anycast Addresses
Multicast:
  Used when a source needs to send data to a group of hosts.
  A single packet is delivered to all members of the group.
  Example: Online video conference or live streaming.
  Relationship: One-to-Many.
Anycast:
  Assigned to multiple devices or servers.
  Packet is delivered to the nearest device (shortest path).
  Commonly used by ISPs for load balancing.
  Relationship: One-to-Nearest.

## Slide 8
Advantages and Disadvantages of IPv6
Advantages:
  Stronger Security: Built-in IPSec provides encryption, authentication, and data integrity.
  Huge Address Space: Solves IPv4 exhaustion.
  Better Performance: Simplified headers, improved routing.
  End-to-End Communication: No need for NAT (Network Address Translation).
Disadvantages:
  Transition Issues: IPv4 and IPv6 are not directly compatible.
  Conversion takes time due to widespread IPv4 usage.
  Implementation Cost: Upgrading devices and software requires investment.

## Slide 9
Thank You