## Slide 1
IPV6

## Slide 2
  An IPv6 address is 128 bits (16 bytes) long, compared to 32-bit IPv4.
  Written in Hexadecimal Colon Notation.
  Divided into 8 blocks of 4 hexadecimal digits (16-bit each).
  Example:
  2001:0db8:85a3:0000:0000:8a2e:0370:7334.
IPV6 ADDRES

## Slide 3
  IPv6 addresses can be long, but abbreviation makes them shorter.
  Leading zeros in each block can be removed.
  Example: 0074 → 74, 000F → F.
  Consecutive zero blocks can be replaced by ::.
  Example: 2001:0db8:0000:0000:0000:0000:0370:7334 →
  2001:0db8::0370:7334.
ABBREVIATION RULES

## Slide 4
IPV6 ADDRESS SPACE
Categories include:
  Unicast – One-to-one communication.
  Multicast – One-to-many communication.
  Anycast – One-to-nearest communication.
  Reserved addresses – Special purposes.
  Local addresses – For private/internal networks.
Addresses are divided into categories by prefix bits.

## Slide 5
  Used for unique device identification (like IPv4 addresses).
  Provider-based unicast (most common):
    Includes fields such as Type ID, Registry ID, Provider ID, Subscriber ID, Subnet ID, Node ID.
    Example: Identifies ISP → subscriber → subnet → device.
  Geographically-based unicast – planned for future use.
  Ensures each device has a globally unique address.
UNICAST Addresses

## Slide 6
MULTICAST & ANYCAST Addresses
  Used when one sender needs to reach many receivers.
  Two types:
  Permanent (always available, assigned by Internet authorities).
  Transient (temporary, e.g., online meetings or streaming).
Multicast Addresses:
  Similar to multicast but sent to only the nearest member.
  Reduces delay and improves performance.
  Example: User request goes to the nearest ISP router instead of all routers.
Anycast Addresses:

## Slide 7
RESERVED & LOCAL Addresses
  Unspecified (::) – used when device doesn’t yet know its address.
  Loopback (::1) – used by a host to test itself.
  Mapped / Compatible – helps during IPv4 ↔ IPv6 transition.
Reserved Addresses:
  Link-local – used inside a single subnet (automatic assignment).
  Site-local – used inside an organization with multiple subnets.
  Provide private communication within local networks.
Local Addresses

## Slide 8
THANK YOU